LTU

SVM

Perceptron

Limited Computational Power

Unit ( )

Multi-Layer Perceptron
w

Layer 1

Feed-forward data-flow diagram

D1:
Input x
Output ŷ

Layer 2

yi = sign(Σi wij xi -θ)
E(w) = Σp 1/2 ║ŷ^(?) - y^(p) ║^2

sign = a function retuning +1 or -1 depending on wether it's input is positive or negative (abbreviated to s)

ŷ(x;w)

1

s(y) = 1/(1+e^-y)
∇w E = (∂E/∂wi)i
∇E exists
How can we calculate this efficiently?
With Constant

y
1/2
0

Aside:
Bad formula, quick and dirty derivative calculation

+ 0(h^2)
h = 0.001

=(f(x+h) – f(x-h))/2h
f(x) = limh->0 ( f(x+h) – f(x))/h

dim w = n
Overhead to calculate ∇E : (time to calculate E) * (dim w)

Backwards propogation of errors:
(Reverse mode accumulation automatic differentiation)
(time to calculate E) * (dim w)

    3 (safe with a 3)

y

V2
V1
V
output

. ^2

E

V'' = (∂ E) /V
D1:	ŷ

* 1/2
 V''1 =1/2

E'' = 1
W''i = (∂ E)/(∂ wi)

V''2 = V''1 (2V2)

Trick: (Fan out)
Vi

F

Xf'
Vj
V''j
V''i
Vj =f(vi)
V''i = (∂E) /(∂Vi) = (∂E) /(∂Vj) * (∂Vj) /(∂Vi)
= v''j f'(vi)

V
V''

V1
V''1

V2
V''2

+

V1
V2
V''1 = U''V2
V''2 = U''V1

*

U
U''
V1 = V2^2
V''1 = (∂E) /(∂V1)
V''2 = (∂E) /(∂V2)
      = (∂E) /(∂V1)* (∂V1) /(∂V2)

      = (V''1)(2v2)